SOFTWARE RELEASE DOCUMENT

----------------------------------------------------------------------------
 Product Name     Integrity XC System NonStop Clusters for SCO UnixWare

 Product Number   T5649D10IPM20

 Part Number      421040-001

 Softdoc Date     1 December 1998
----------------------------------------------------------------------------

Release Summary

This release of NonStop Clusters® for SCO® UnixWare® is an update to the
D10IPM10 release of the Tandem® single system image (SSI) UNIX® clustering
technology. This release includes features such as:

   * Cluster-wide (SSI):

        o Access to storage devices

        o Access to other system resources

        o Swap/paging service

        o System V IPC, devices, pipes

        o STREAMS access

        o Parallel networking

        o Cluster time synchronization

        o Distributed processes

   * Journaled file system

   * Disk mirroring using the Compaq SMART-2DH controller

   * File system failover

   * Application restart and failover

Product Table of Contents

This document contains descriptions of the following product components.
 Comp T Number  Product Component      Comp T Number  Product Component

 T5649D10IPM20  NonStop Clusters

Superseded IPMs

This release supersedes the D10IPM10 release of NonStop Clusters.

Requisite IPMs

None

Required Hardware

None

Required Firmware

Version TPN 131790 A03-03 of the Tandem ServerNet SAN Switch.

Required Software

T5649D10 NonStop Clusters for SCO UnixWare operating system.

T5649D10IPM10 NonStop Clusters for SCO UnixWare operating system.

T5649D10IPM20 NonStop Clusters for SCO UnixWare operating system.

SCO UnixWare 2.1.2 (supplied with the original factory shipment)

Required Disk Space

Minimum 2 GB

Manuals

The manuals associated with this product are defined in the following table.
 Part Number Manual Title

 420938-001  Integrity XC System NonStop Clusters for SCO UnixWare System
             Administrator's Guide

 420941-001  Integrity XC System Site Preparation and Hardware Installation

 421180-001  Documentation Notes for Integrity XC System NonStop Clusters
             for SCO UnixWare Administrators Guide

Migration Considerations

None

Installation Considerations

Refer to this softdoc for D10IPM20 installation instructions, and to the
"Known Problems" section of this softdoc for installation considerations.

General Notes

  1. An on-line version of this softdoc will be updated as new information
     is available about the product. The current softdoc for this product is
     viewable on the World Wide Web and is accessed from a link on the
     softdoc index page:

     https://www.austx.tandem.com/softdocs/

     These pages are password-protected. At the prompts, enter "Tandem" for
     the userID and "!ntegr1ty" for the password. The server is
     case-sensitive, so note the uppercase T in the userID and the
     exclamation point and number 1 in the password.

Trademarks

Tandem, Integrity, NonStop, NonStop-UX, and the Tandem logo are trademarks
or registered trademarks of Tandem Computers Incorporated in the United
States and/or other countries.

Oracle is a registered trademark, and Oracle 7 is a trademark of Oracle
Corporation.

Compaq, ProLiant, and the Compaq logo are trademarks or registered
trademarks of Compaq Computers Incorporated in the United States and/or
other countries.

SCO, The Santa Cruz Operation, UnixWare, and the SCO logo are trademarks or
registered trademarks of Santa Cruz Operation Incorporated in the United
States and/or other countries.

INFORMIX is a registered trademark and ONLINE Dynamic Server is a trademark
of Informix Software Incorporated.

UNIX is a registered trademark in the United States and other countries,
licensed exclusively through X/Open Company Limited.

NFS is a registered trademark of Sun Microsystems, Inc.

Veritas, VxFS, and VxVA are registered trademarks of Veritas Software
Corporation.

UniSoft is a registered trademark of UniSoft Corporation.

All other brand and product names are trademarks or registered trademarks of
their respective companies.

Copyright Notice

Copyright (c) 1998, Tandem Computers Incorporated.
All rights reserved.

The computer program listings, specifications and documentation herein are
the property of Tandem Computers Incorporated or a third party supplier and
shall not be reproduced, copied, disclosed, or used in whole or in part for
any reason without the prior express written permission of Tandem Computers
Incorporated.
----------------------------------------------------------------------------

Product Component: NonStop Clusters - T5649D10IPM20

----------------------------------------------------------------------------

Description

This is the D10IPM20 release of the NonStop Clusters for SCO UnixWare
operating system for Compaq ProLiant Intel based PCs of the single-system
image, distributed operating system.

Contents

The following packages belong to this component:
 Package   Version   Package Description
 D10IPM20  D10IPM20  NonStop Clusters software
 nscman    D10IPM20  NonStop Clusters manpages
 D10I20doc D10IPM20  NonStop Clusters software release document

Notes

  1. Included in this release is a document entitled Documentation Notes for
     the NonStop Clusters Administrator's Guide. This document contains
     information that was unavailable when the manual was printed. Refer to
     the Documentation Notes for the latest changes to the installation
     procedures in Chapter 3 of the manual and the recovery procedures in
     Appendix B of the manual.

  2. D10IPM20 includes an Increased Reliable Disk Capacity Feature.

     This feature increases the maximum disk capacity of NonStop Clusters
     for UnixWare. Maximum disk capacity is increased by a factor of 3 by
     adding support for multiple reliable disk subsystems. Previous releases
     of NonStop Clusters supported a single reliable disk subsystem that
     provided disk and file system failover between the primary and backup
     root nodes. This feature allows the configuration and management of two
     additional reliable disk subsystems connected between pairs of
     dependent nodes. The additional reliable disk subsystems will provide
     the equivalent functionality for disk and file system failover between
     dependent nodes that was previously provided between primary and backup
     root nodes.

     More information on this new feature is described in the Integrity XC
     System Site Preparation and Hardware Installation manual in Appendix B,
     System Upgrades.

     The default system configuration provides sufficient memory resources
     to perform filesystem failover under most conditions. However, it is
     possible for filesystem failover to fail to complete due to
     insufficient memory and thus hang the cluster. This condition can be
     avoided by increasing the DESFREEBYTES and LOTSFREEBYTES tunables
     sufficiently to ensure the system has adequate memory to perform the
     filesystem failovers. A reasonable rule of thumb is to add 30KB per
     failover-capable filesystem to the current values of DESFREEBYTES and
     LOTSFREEBYTES.

  3. Real time applications are not supported in this release. They may
     cause the cluster to hang.

  4. Mounting a filesystem with the chard or charddup mount options may
     display the following message on the system console when there isn't a
     node available to provide the backup cache for that filesystem.

     Message:

     WARNING: Error 11 mounting backup cache vfsp 0xXXXXXXXX

     This message commonly appears when booting the root node with the
     tnc_rootopt bootstrap parameter set to 0x84000 (chard,intr) or 0x104000
     (charddup,intr). This message also appears when mounting any filesystem
     with the chard or charddup options and there are no backup cache nodes
     available for the filesystem (either none were specified with the bkup
     mount option or those specified have not joined the cluster).

     As specified in the mount(1m) manual page, the lack of a backup cache
     for a chard or charddup-mounted filesystem may result in writes to that
     filesystem being performed synchronously to disk to provide the level
     of data integrity associated with the respective mount option. If/when
     a node joins the cluster to provide the backup cache for the chard or
     charddup-mounted filesystem, writes to that filesystem will no longer
     be forced to be synchronous to disk. For example, if the root node is
     mounted with chard or charddup, writes may be performed synchronously
     to disk until the secondary root node joins the cluster to provide the
     backup cache for the root filesystem.

  5. The following INFORMIX OnPerf menu options are not supported in this
     release:

        o physical processor metrics

        o physical processor tool

     This is a result of differences between UnixWare and NonStop Clusters.
     The current workaround is to use the sar utility.

     Also, the OnPerf utility may give the following error:

     Couldn't open data file /var/adm/metreg.data

     This error is also a result of the differences between UnixWare and
     NonStop Clusters. The current workaround is to start OnPerf with
     standard error messages routed to "/dev/null".

     No fix is currently planned for the preceding problems. OnPerf will
     report proper performance information on INFORMIX metrics. To obtain
     machine specific performance information, use the sar utility.

  6. Two tunable parameters that are associated with system panic dump
     generation are still applicable for the D10IPM20 release.

     SYSDUMP_SELECTIVE:

     Flag value that determines if the system will dump all pages (0), or
     selectively dump only pages mapped in the kernel (1). The default value
     is 1: to generate a selective dump, occupying much less space, rarely
     losing information.

     SYSDUMP_POLL:

     Flag value that determines if the system will dump relying upon the
     disk interrupt (0), or poll for I/O completion (1). The default value
     is 1: to poll with disk interrupt disabled, in case the interrupt is
     shared with other devices which might stop the dump.

  7. Software patches, or PTFs, from SCO for UnixWare are not supported with
     NonStop Clusters. NonStop Clusters must be installed over UnixWare
     2.1.2. No SCO PTFs are to be installed before or after NonStop Clusters
     is installed.

  8. The Site Preparation and Hardware Installation manual describes a
     Japanese PDU that may not be available at D10IPM20. A North American
     low-voltage PDU will be substituted until the Japanese PDU is available
     for shipment.

The following known problems have workarounds:

  1. Boot loop resolution needed on base SCO UnixWare installation (PTS
     35084).

     Symptom: System attempts to rebuild and reboot continuously after
     system installation.

     Workaround: The following method can be used to resolve this situation
     should it occur.

     The following message will repeatedly appear on the console screen
     immediately after a system installation or reconfiguration:

     The UNIX Operating System kernel will now be rebuilt to incorporate
     recent configuration changes.

     Press the ENTER key when ready or the ESC key to stop.

     You should press the ESC key. At the prompt, enter the command "#
     resmgr". Examine the output to find the following entries:

     19 cpqsc 0 5 4 10 7000 70ff 40101000 401010ff - - 4 0x1000000F 0 - 1

     21 ida 2 5 4 5 8000 80ff c8000 cbfff - - 4 0xE11AE10 - - 2

     22 ide 2 5 3 14 1f0 1ff 10000 10001 -1 - 0 - - - -

     NOTE: The key numbers (the first field) may not match the preceding
     example.

     The third field (unit number) is conflicting. The unit numbers are
     incorrect and must be manually changed to the following correct values.

     KEY UNIT UNIT#.

     <key> cpqsc 0 ...

     <key> ida 2 ...

     <key> ide 1...

     The first field is the "KEY". Using the appropriate KEY, modify the
     appropriate unit number entry to match the preceding values. In this
     example, key is 22 and ide is changed from unit 2 to unit 1.

     resmgr -k 22 -p "UNIT" -v "1"

     Commit the configuration changes by entering the command
     "/etc/conf/bin/idconfupdate -f". Reboot the system and allow it to
     rebuild the UNIX operating environment.

  2. Unable to copy wild card files from a mounted file system on a
     CM-1300(PTS 34195).

     Symptom: When trying to copy several files using the wild card symbol,
     the files do not copy correctly or it seems to "hang" and not copy
     anything.

     This only occurs when using ksh while running on a file system NFS
     mounted from a CM-1300. It works correctly on all other platforms.

     Workaround: Do not attempt file locking (for example, use csh) when
     accessing files NFS mounted from a CM-1300.

  3. keepalive has no interface for "shutdown" scripts. (PTS 36470).

     Symptom: Currently, keepalive's only interface to tell a process to do
     a controlled shutdown is via a SIGTERM. This does not work well with
     processes that should be shut down another way,(e.g., lpsched).

     Workaround: Unregister the process with keepalive. Then use whatever
     shutdown procedure is appropriate for the process.

  4. /etc/rc2.d/S51nis file missing domain name when created by "pkgadd nis"
     from SCO CDROM (PTS 36525).

     Symptom: Domain name will not have a valid entry.

     Workaround: In the file "/etc/rc2.d/S51nis", change the line:

     domain

     to:

     domain <domainname>

     where <domainname> is the internet domain name for the machine.

  5. Installing NIS after NonStop Clusters overwrites "/etc/init.d/nis".
     This results in the NIS daemons no longer being registered with
     keepalive (PTS 36767).

     Symptom: NonStop Clusters does not install NIS by default. When pkgadd
     is used to install NIS from the SCO 2.1.2 CD, it replaces the Tandem
     version of the file "/etc/init.d/nis". As a result, all the changes
     that are required for spawndaemon are lost and NIS does not failover.

     Workaround:

       1. Copy the file "/etc/init.d/nis" to "/tmp/nis" before installing
          NIS.

       2. Install NIS from the SCO CD on each cluster. Do not configure NIS
          when it is installed, as that will be overwritten by step 3.

       3. Copy the file saved in "/tmp/nis" to "/etc/init.d/nis" to each
          cluster.

       4. Run "ypinit" with the correct option to configure each cluster.

  6. System will not boot when one RAID cabinet is powered off (PTS 36770).

     Symptom: When one of the disk cabinets is powered off at boot time, and
     the F1 prompt is disabled, the entire disk array is disabled causing
     the system boot to fail.

     Workaround: The following configuration changes will enable the F1
     prompt, change the recovery server option status, and prevent this
     problem. If you make the following configuration changes, it will be
     necessary to type F1 during boot to allow the cluster to boot when one
     RAID cabinet is powered off. However, in many cases, this is preferable
     to failing to boot at all.

       1. Shutdown the cluster.

       2. Power off all nodes.

       3. Power on node 1, select F10 during the boot sequence to execute
          utilities from the System Partition.

       4. At the "Main Menu", type <ctl-a> to select "Advanced Mode".

       5. At the "Main Menu", select System Configuration.

       6. From the "System Configuration" menu, select Configure Hardware.

       7. From the Configure Hardware menu, select Review or Modify Hardware
          Settings.

       8. From the next menu, select "View and Edit Details".

       9. Under "Slot? - Compaq SMART-?? Array Controller", highlight
          "Online Recovery Server Status". If "Primary" is selected, press
          <enter>, select "Recovery", and press <enter>.

          Note: If you get the "Write Cache Disable Warning" window, then
          ignore it and press <enter>.

      10. Under "Advance Feature", find the entry "F1 boot prompt", if
          disabled, press <enter>, and select <enabled>, then press <enter>.

      11. Press F10 to continue.

      12. Back at the previous menu, select "Save and exit".

      13. Select "Save the configuration and restart the computer".

      14. Press <Enter> to reboot.

      15. Power on the other nodes in your cluster.

  7. Token deadlock in forced unmount (PTS 37167).

     Symptom: Under rare conditions, if you do a "umount -o force" on a
     running file system, it can hang indefinitely.

     Workaround: Do not forcibly unmount running file systems.

  8. force unmount of NFS FS with yet-to-be-noticed downed server loops
     forever in cfs_hide_cnodes (PTS 37238).

     Symptom: When trying to unmount a file system using "umount -o force",
     a downed server may hang.

     Workaround: Do not force an unmount with a downed NFS server.

  9. Closes done from process exit on downed hardmounts are
     non-interruptible (PTS 38167).

     Symptom: Process with files on a downed hardmount cannot be killed.

     Workaround: Remount or forcibly unmount the file system.

 10. Unshare of downed file system hangs system shutdown (PTS 38283).

     Symptom: Shutdown hangs on a system that has a downed, shared,
     hardmount file system.

     Workaround: Use "umount -o force" to bring the file system down.

 11. NonStop Clusters OS: unexpected defaults while running: console
     keyboard and mouse lockup on UnixWare 2.1.1 upgrade. Customer reported
     defect. (PTS 38293).

     Symptom: On some platforms, after adding the UnixWare 2.1.1 update
     package (update211), the local keyboard and mouse will not respond
     after rebooting the new kernel. This defect corrects itself after
     installing the UnixWare 2.1.2 package.

     Workaround: The user can telnet into the system, continue to pkgadd the
     update212 package, and reboot the system. Alternatively, if networking
     is not setup or otherwise unavailable, it may be possible to boot a
     2.1.0 kernel (saved as unix.old during the 2.1.1 upgrade) and perform
     the 2.1.2 pkgadd using the old kernel.

 12. new_rem_swapfile() can deadlock with tnc_anon_resv_adjust() over
     registrar locks (PTS 38390).

     Symptom: If the cluster has been running under a significant memory
     load, the root node appears "hung".

     Workaround: Ensure there is always sufficient swap space on each node
     to satisfy the peak per-node memory load.

 13. UX:init: ERROR: Command is respawning too rapidly. Check for possible
     errors. id: co "/usr/lib/saf/ttymon -g -v -p "Console Login: " -d
     /dev/console.3 -l console" (PTS 38407).

     Symptom: After adding the D10IPM20 package, the following message may
     appear on the primary node's console prior to rebooting the node:

     UX:init: ERROR: Command is respawning too rapidly. Check for possible
     errors.

     id: kp "/sbin/keepalive -t 10 -P 1 -S 2"

     Workaround: If this message should occur, remove any core files in the
     / (root) directory which may have been created during the time the
     preceding messages was displayed. The message itself can be ignored.

 14. cnet Adapter Check causes the whole cluster to hang (PTS 38666).

     Symptom: When installing the Oracle package, mounting the Oracle
     distribution CD on one node and the Oracle install scripts are executed
     from a different node, the following error may occur:

     WARNING: cnet: unit 0: Adapter Check interrupt 100002!

     Interface 0 in slot 16 has failed.

     Attempting to restart.

     When this happens, the cluster may hang.

     Workaround: Ensure the Oracle CD is mounted on the node 1 CD-ROM drive
     and that the install scripts are executed on node 1. To ensure the
     Oracle install scripts are executed on node 1, use the following onnode
     commands:

     onnode -p 1 ./start.sh

     onnode -p 1 ./orainst /c

     This may happen with other applications that access the CD-ROM drive
     heavily.

 15. Running out of kernel virtual can cause poolrefresh to spin on cpu
     (hangs UP systems) (PTS 39941).

     Symptom: Backup cache node is a uniprocessor system and is hung after
     heavy activity on a chard or charddup-mounted filesystem.

     Workaround: Increase the SEGKMEM_PERCENT tunable. Default is 55. Try
     increasing by about 50%, e.g. try 80.

 16. Receive error message when booting the dependent node from the boot
     floppy. Currently not in the PTS database.

     Symptom: When booting from the Secondary Boot Diskette, you receive the
     error message, "/sbin/metreg: getksym error = 154".

     Workaround: This is normal behavior. The message only occurs when you
     are installing the node from the boot floppy. Just ignore the message.

New Features

The following new features are supported with the NonStop Clusters D10IPM20
release:

   * ProLiant 1850R/400 support.

   * ProLiant 5500R/400 support.

   * ServerNet SAN online diagnostics.

   * Additional Disk Capacity

Problems Corrected

  1. LCCrq05483:auditrpt cannot read rfork/migrate/rexec entries into the
     log file.
     (PTS 31775, No TPR, Severity 2)

  2. Standalone build is broken cause uts/io/tdmpci/pci.h overwrites
     uts/io/autoconf/ca/pci/pci.h.
     (PTS 32887, No Tpr, Severity 2)

  3. Interface direct routes are not handled correctly.
     (PTS 33464, No TPr, Severity 2)

  4. CLMS needs node transition vector support.
     (PTS 35621, No TPR, Severity 3)

  5. TCP hangs on inp_rwlck while running VSTS test.
     (PTS 36081, No TPR, Severity 2)

  6. pdimkdev makes devices with controller number 65534.
     (PTS 36203, No TPR, Severity 2)

  7. Spurious "too many nodes" reboot from licensing support code.
     (PTS 36204, No TPR, Severity 3)

  8. pkgadd of tcpip_nis.so fails. i.VUF script needs work?
     (PTS 36904, No TPR, Severity 2)

  9. Panic in tcp_respond().
     (PTS 37117, No TPR, Severity 2)

 10. ics_msg_ack_done() kernel panic after a node goes down.
     (PTS 37170, No TPR, Severity 3)

 11. Either "migrate(1)" is not moving processes, or "ps(1)" is not
     correctly reporting them with the -N option.
     (PTS 37319, No TPR, Severity 1)

 12. inode table overflow on CD file system.
     (PTS 37509, No TPR, Severity 2)

 13. Panic in bcopy() because of a bad length field in an LWP audit buffer.
     Customer reported defect.
     (PTS 37566, No TPR, Severity 3)

 14. VPROC nodedown hung trying to remove pgrp from nonexistent session.
     (PTS 37711, No TPR, Severity 3)

 15. Hang during nodedown processing after failover - semconv() spinning on
     lock.
     (PTS 37721, No TPR, Severity 3)

 16. /etc/dfs/sharetab seems to get corrupted, causes mount access denial.
     (PTS 37785, No TPR, Severity 2)

 17. Diskadd command is broken.
     (PTS 37993, No TPR, Severity 2)

 18. ASSERTION CAUGHT: ioflag == CPFS_IO_NONE, file: cfs_vm_osi.c, line:
     1139.
     (PTS 37995, No TPR, Severity 2)

 19. Downgrading tokens at cli@svr doesn't clean backup cache anymore.
     (PTS 37997, No TPR, Severity 2)

 20. Implement Parallel NeRD performance changes.
     (PTS 38001, No TPR, Severity 2)

 21. fuser hangs in uts_fusers() on a down filesystem.
     (PTS 38013, No TPR, Severity 2)

 22. cfsbc_sync_hplist() needs to handle trylock failure of svrcfstok's
     stateloc.
     (PTS 38075, No TPR, Severity 2)

 23. Normal cfs pageouts should not set critical memory priority.
     (PTS 38099, No TPR, Severity 2)

 24. HANFS: mountd can hang on down CFS HARD mount preventing new NFS
     mount/unmount/showmount.
     (PTS 38101, No TPR, Severity 2)

 25. EXNFS DEBUG: ASSERTION CAUGHT: vfsp->vfs_count > 0, file: cfs_chard.c,
     line: 569.
     (PTS 38126, No TPR, Severity 3)

 26. NFS mount can deadlock filesystem failover.
     (PTS 38129, No TPR, Severity 2)

 27. Sleeping operations on down hardmounts now woken up when forcibly
     unmounted.
     (PTS 38165, No TPR, Severity 2)

 28. NonStop Clusters OS: abending while running: open(2) causes cluster
     crash. Customer reported defect.
     (PTS 38247, TPR # 980626-1633-16640, Severity 2)

 29. EXNFS client: ASSERTION CAUGHT: i < MAXIDS, file: cfs_hm.c, line: 1167.

     (PTS 38249, No TPR, Severity 3)

 30. ASSERTION CAUGHT: !swappedin, file: rwsleep.c, line: 1257.
     (PTS 38253, No TPR, Severity 2)

 31. Keepalive and Spawndaemon do not process partially read and written
     messages.
     (PTS 38304, No TPR, Severity 2)

 32. EX NFS client/server: statd restart is broken.
     (PTS 38465, No TPR, Severity 2)

 33. mountd needs to be added to the package for D20.
     (PTS 38468, No TPR, Severity 1)

 34. Double failure of root server and root backup cache node deadlocks root
     failover.
     (PTS 38485, No TPR, Severity 2)

 35. Cluster20 hung while serving as an IP server for netbench, cthon and a
     peer in the tcp_test. I was able to log in, but never received a
     prompt. All three nodes were effected.
     (PTS 38656, No TPR, Severity 3)

 36. Clms can send rpc to itself while its taking over as the new clms
     master.
     (PTS 38679, No TPR, Severity 2)

 37. EXNFS client: new CLIENT field ch_addr not set by clget() (no port info
     to CFS client).
     (PTS 38685, No TPR, Severity 2)

 38. Assertion caught: getpl() == PLBASE, file ublock.c, line 276.
     (PTS 38696, No TPR, Severity 2)

 39. PANIC: kernel-mode address fault on user address 0x4
     (cfs_blkrsrv_giveback_svr).
     (PTS 38730, No TPR, Severity 2)

 40. NFS panic in exportfs().
     (PTS 38791, No TPR, Severity 2)

 41. efork() hangs when fork() returns EAGAIN.
     (PTS 38794, No TPR, Severity 2)

 42. Inconsistent return values from fsck after failover.
     (PTS 38801, No TPR, Severity 2)

 43. cmount -p option doesn't wait for mounts to complete.
     (PTS 38880, No TPR, Severity 2)

 44. svrcfstok_policy() can deadlock failover.
     (PTS 38887, No TPR, Severity 2)

 45. NOTICE: ASSERTION CAUGHT: !(cp->c_flags & CHIDDEN), file: cfs_subr.c,
     line: 801.
     (PTS 38901, No TPR, Severity 2)

 46. EX NFS client: Not enough XIDs allocated for writes when NFS code does
     read-to-do-write.
     (PTS 38904, No TPR, Severity 2)

 47. Panic caused by failing over during mmap of MANDLOCK file.
     (PTS 38927, No TPR, Severity 2)

 48. SIOCGIFALL doesn't return all interfaces because ifnet's not sorted by
     if_index properly.
     (PTS 38952, No TPR, Severity 2)

 49. Intra-cluster TCP connections are not reset when one endpoint is lost
     and connection idle.
     (PTS 38953, No TPR, Severity 2)

 50. crfs_open_0() has memory leak.
     (PTS 39015, No TPR)

 51. Retry loop (added via TDM_BUG_FIX) in nfs_async_start() panics due to
     undone buf_t.
     (PTS 39018, No TPR, Severity 2)

 52. Part of Accurate Idle facility omitted from Package Added kernels.
     (PTS 39025, No TPR, Severity 2)

 53. kmem_alloc() panic during vproc nodedown.
     (PTS 39072, No TPR, Severity 2)

 54. SPAD needs to be modified to support VIA emulator.
     (PTS 39079, No TPR, Severity 2)

 55. Error handling when removing local disk from cluster needs to be
     improved. Customer reported defect.
     (PTS 39102, No TPR, Severity 3)

 56. EXNFS client: PANIC: svrgivebacknode: Specified agent NOT found!
     (PTS 39115, No TPR, Severity 3)

 57. SPAD should use the standard PCI interface and support autoconfig.
     (PTS 39130, No TPR, Severity 2)

 58. NOTICE: ASSERTION CAUGHT: "%eax > $_A_PLBASE", file: intr_p.s,
     assertion #: 3.
     (PTS 39160, No TPR, Severity 2)

 59. Top of tree pkgadd fails.
     (PTS 39168, No TPR, Severity 3)

 60. Window in use of clms_get_cluster_num_nodes() following
     clms_get_tnc_nodelist().
     (PTS 39206, No TPR, Severity 2)

 61. Function aadReadConfigFile() must need configuration parameters for the
     resource acquisition program.
     (PTS 39221, No TPR, Severity 3)

 62. tcp_output() fastpath logic needs to use loopback for local addresses.
     (PTS 39226, No TPR, Severity 2)

 63. disksetup w/surface analysis on dependent node causes root node panic.
     (PTS 39227, No TPR, Severity 3)

 64. Ifdef test around include files incorrect in spad.h - breaks build.
     (PTS 39228, No TPR, Severity 3)

 65. Which node the cluster IP address is on is not guaranteed. Customer
     reported defect.
     (PTS 39239, No TPR, Severity 2)

 66. The inet daemon does not restart after a failover. Customer reported
     defect.
     (PTS 39241, No TPR, Severity 2)

 67. If route.d is running the node routing tables get messed up. Customer
     reported defect.
     (PTS 39244, No TPR, Severity 2)

 68. swap -d /dev/swap.<node_num> fails.
     (PTS 39258, No TPR, Severity 2)

 69. Need to check whether the resource acquisition script is running before
     trying to kill it.
     (PTS 39278, No TPR, Severity 2)

 70. Panic in strclose() when strelwp_findhash() returns NULL.
     (PTS 39331, No TPR, Severity 2)

 71. Keepalive doesn't restart PPM when it is killed.
     (PTS 39334, No TPR, Severity 2)

 72. Init must special-case its own node to avoid running generic nodeup
     there.
     (PTS 39343, No TPR, Severity 3)

 73. When recovering a query session (through FDS) if the fd cannot be
     retrieved the PPM still tries to build a session around the bogus fd.
     (PTS 39345, No TPr, Severity 2)

 74. The 'tnc' rc script wasn't checked in.
     (PTS 39347, No TPR, Severity 3)

 75. Remove sequencing from backup cache support.
     (PTS 39349, No TPR, Severity 2)

 76. rdev_size() local path broken.
     (PTS 39373, No TPr, Severity 2)

 77. Cmount remounts file system incorrectly when failing over from an even
     to an odd node.
     (PTS 39385, No TPR, Severity 2)

 78. Nodedown hung waiting for vproc slave daemon processing that was
     throttled due to low memory.
     (PTS 39405, No TPR, Severity 2)

 79. CLMS doesn't handle CLUSTERNODE_SHUTDOWN state properly.
     (PTS 39417, No TPR, Severity 3)

 80. Init respawns ttymon on down node.
     (PTS 39424, No TPR, Severity 3)

 81. NonStop Clusters D10 - should cvip be used as default sending ip
     address in outgoing ippackets? Customer reported defect.
     (PTS 39457, TPR # 980929-754-16102, Severity 2)

 82. Code-inspection-induced CLMS change breaks failover.
     (PTS 39474, No TPR, Severity 3)

 83. Spawndaemon gets a 'Segmentation Fault - core dumped'.
     (PTS 39481, No TPR, Severity 2)

 84. CLMS tells clients about key secondaries early, but doesn't tell the
     secondaries.
     (PTS 39482, No TPR, Severity 3)

 85. Processes added to keepalive are not always registered permanently.
     (PTS 39483, No TPR, Severity 2)

 86. Race in TIOCPGRP processing in strioctl().
     (PTS 39485, No TPR, Severity 2)

 87. clms_ready_key_nodes() skips secondaries.
     (PTS 39491, No TPR, Severity 3)

 88. Race in nodeup of secondary key server node.
     (PTS 39506, No TPR, Severity 3)

 89. Informing key nodes from master nodeup may race with key node join.
     (PTS 39523, No TPR, Severity 2)

 90. After failover ipcs indicates that SHM segments on surviving node are
     gone. Customer reported defect.
     (PTS 39539, No TPR, Severity 2)

 91. CLMS cluster statistics not maintained properly by API support.
     (PTS 39544, No TPR, Severity 2)

 92. "arscli -o watch" does not register PPMs with Keepalive using a node
     set.
     (PTS 39553, No TPR, Severity 2)

 93. ASSERTION CAUGHT: ATOMIC_INT_READ(&tp->t_inpcb->inp_qref) > 0, file:
     tcp_subr.c, line 258.
     (PTS 39581, No TPr, Severity 2)

 94. Keepalive's mmapped file got corrupted.
     (PTS 39586, No TPR, Severity 2)

 95. Panic in ip_control() SIOCSIFFLAGS route handling.
     (PTS 39590, No TPR, Severity 2)

 96. NonStop Clusters OS: abending while running: panicstr: readmem error:
     user address for kernel process. Customer reported defect.
     (PTS 39594, PR # 981021-712-16640, Severity 3)

 97. BASE EX NFS: Getting cli EDEADLK when svr lockd unavailable (problem
     for failover.
     (PTS 39603, No TPR, Severity 2)

 98. Onnode fails in nodedown/node.generic when recovery node is still
     coming up.
     (PTS 39608, No TPR, Severity 2)

 99. CLMS routines rclms_api_newstate() and rclms_send_nodeup_info() can
     deadlock.
     (PTS 39630, No TPR, Severity 2)

100. Keepalive: with -i option can fail because it mistakenly thinks another
     keepalive present.
     (PTS 39631, No TPR, Severity 2)

101. Keepalive calls map_ka_data() with data_fd variable uninitialized.
     (PTS 39632, No TPR, Severity 2)

102. KEEPALIVE: verify_ka_not_running() doesn't check current pid like
     find_other_ka().
     (PTS 39633, No TPR, Severity 2)

103. Racing nodedowns can hang init.
     (PTS 39635, No TPR, Severity 3)

104. Make file in the PPM directory does not remake the PPM when a file gets
     changed.
     (PTS 39668, No TPR, Severity 2)

105. Keepalive doesn't reopen syslog after creating primary Keepalive.
     (PTS 39670, No TPR, Severity 2)

106. The CLMS master doesn't send nodedown messages to all the nodes it
     should.
     (PTS 39672, No TPR, Severity 3)

107. Long delay in ics_llnodeup() causes other nodeups to fail.
     (PTS 39673, No TPR, Severity 3)

108. rpcbind warmstart (-w) with restarting mountd gives errors to client.
     (PTS 39716, No TPR, Severity 2)

109. The ics_nodedown() in clms_client_startup_node() races with
     rclms_rgp_add_node().
     (PTS 39725, No TPR, Severity 2)

110. clms_get_up_nodelist() needs to get HALF_DOWN nodes, too.
     (PTS 39726, No TPR, Severity 2)

111. PANIC: kernel-mode address fault on user address 0x0 -> in
     cfsbc_copytobuf().
     (PTS 39730, No TPR, Severity 2)

112. Unisoft: Touch command failed to change(touch) date.
     (PTS 39745, No TPR, Severity 2)

113. Deadlock when spawning processes early in nodeup.
     (PTS 39749, No TPR, Severity 2)

114. BASE BUG: panic in do_ERROR() as called by free_zero() because of
     q->q_ptr == NULL.
     (PTS 39753, No TPR, Severity 2)

115. Init doesn't shoot coming-up nodes properly after failover.
     (PTS 39796, No TPR, Severity 2)

116. CLMS and the API's system call doesn't support changing state to
     KCLEANUP.
     (PTS 39797, No TPR, Severity 2)

117. Keepalive needs to support unregistration by daemon name and argument
     list.
     (PTS 39815, No TPR, Severity 2)

118. Need to make cfs caching policy tunable (cfs_delay_writes).
     (PTS 39839, No TPR, Severity 2)

119. CLMS client doesn't check for wrap of trans hist when getting it from
     the master.
     (PTS 39854, No TPR, Severity 3)

120. Multiple open/single write in charddup,bkup failure after writes
     complete results in error.
     (PTS 39875, No TPR, Severity 2)

121. Signal forwarding could result in NO_JOB_FORWARD ops stopping and
     hanging failover.
     (PTS 39908, No TPR, Severity 2)

122. Comparison takes precedence over bitwise-and near line 823 in
     spawndaemon.c.
     (PTS 39911, No TPR, Severity 2)

123. cspecvp() can loop forever on a down softmount.
     (PTS 39946, No TPR, Severity 3)

124. backup cache unmount needs to wait for in-progress file syncs.
     (PTS 39949, No TPR, Severity 2)

125. Window for race in job control handling in issig() vs.
     cancel_jobctrl().
     (PTS 39968, No TPR, Severity 2)

126. loop/hang on dependent node failover test.
     (PTS 39990, No TPR, Severity 3)

Known Problems Remaining

  1. Stale RPC delivered after a nodedown.
     (PTS 36062, No TPR, Severity 2)

  2. Races in forced unmount need to be examined.
     (PTS 36343, No TPR, Severity 2)

     Some issues are present where forced unmount of a file system can
     panic. Most likely, NFS would have problems.

  3. select() supposed to time out in 5 seconds but does not return for over
     1 minute.
     (PTS 36401, No TPR, Severity 2)

  4. Stale cshandle after failover.
     (PTS 36457, No TPR, Severity 2)

  5. /tmp, /var/tmp, /usr, and /var should all be hard mounted separate file
     systems.
     (PTS 36659, No TPR, Severity 2)

  6. The regroup function rgp_select_cluster() should factor in the
     importance of root-fs nodes.
     (PTS 36830, No TPR, Severity 2)

  7. cli_ipcname_getid() has failover race; CMS has a similar problem.
     (PTS 37157, No TPR, Severity 2)

     Currently under investigation.

  8. Token deadlock in forced unmount.
     (PTS 37167, No TPR, Severity 2)

  9. Force unmount of NFS FS with yet-to-be-noticed down server loops
     forever in cfs_hide_cnode.
     (PTS 37238, No TPR, Severity 2)

 10. memfs may report out of space due to the way dswap usage is calculated.

     (PTS 37246, No TPR, Severity 2)

     There must be at least as much total swap in the cluster as there is
     total RAM in the cluster. Otherwise, it is possible that shared memory
     segments cannot be created and memfs file systems may report
     out-of-space.

 11. Substantial memory leak found in ics/llics after performing nodedowns.
     (PTS 37262, No TPR, Severity 2)

 12. PANIC in cfs_blkrsrv_svrnodedown().
     (PTS 37292, No TPR, Severity 2)

     Currently under investigation.

 13. Verify that if idbuild fails on shutdown that idcpunix does not
     propagate kernel.
     (PTS 37408, No TPR, Severity 2)

 14. Panic in prreadobjdir after failover.
     (PTS 37528, No TPR, Severity 2)

     Under certain rare conditions during failover, the node taking over
     root/clms/init responsibility panics with the following:

     00: PANIC: kernel-mode address fault

     Crash dump analysis will indicate the faulting thread is in the
     function prreadobjectdir().

     Currently, there is no known workaround.

 15. initprivs/filepriv are not distributed.
     (PTS 37533, No TPR, Severity 2)

 16. NFS client needs to present itself as CVIP for all client messages.
     (PTS 37642, No TPR, Severity 2)

 17. Kernel must reboot automatically for unattended operation.
     (PTS 37795, No TPR, Severity 2)

 18. XDM error log fills /tmp.
     (PTS 37797, No TPR, Severity 2)

 19. PANIC: kernel-mode address fault on user address 0x100.
     (PTS 37918, No TPR, Severity 3)

 20. DEADLOCK: CMS locking must be fixed to prevent nodedown deadlock.
     (PTS 37930, No TPR, Severity 2)

     Possible deadlocks exist in the CMS code during nodedown. There is
     nothing to distinguish these from other possible deadlocks in nodedown.

 21. UX:nfs mount: ERROR: get_addr: (host cluster20, program 100003, version
     2) is not found on any transport.
     (PTS 37966, No TPR, Severity 2)

     Currently under investigation.

 22. Need to fix sorting of routes in rtrequest().
     (PTS 37985, No TPR, Severity 2)

 23. NFS code is cfs_rb_dolocks() creates a bogus cnode.
     (PTS 37990, No TPR, Severity 2)

     Currently under investigation.

 24. EXNFS: A dirty page from CFS as NFS client causes cfs_data_downgrade
     loop.
     (PTS 38002, No TPR, Severity 2)

     This defect will be seen as "hung" processes. Currently, wait for the
     NFS server to come back up. The processes will no longer be "hung".
     Even if NFS is not mounted with "intr", it is rare that the processes
     will not be interruptible.

 25. Failover clusters need CVIP interfaces.
     (PTS 38016, No TPR, Severity 2)

 26. HANFS: Backup locks not rebuilt when backup lock node joins cluster.
     (PTS 38025, No TPR, Severity 2)

     The user will not be able to detect this defect. This occurs if node 1
     fails after node 2 has failed and rejoined the cluster, and if file
     locks are being backed up.

 27. PANIC: Range tokens do not handle 2 GB or higher values.
     (PTS 38177, No TPR, Severity 2)

     This occurs because no single file or disk partition can be larger that
     2 GB. Do not use the "dd" command to copy a disk partition larger than
     2 GB.

 28. ASSERTION CAUGHT: !swappedin, file: rwsleep.c, line: 1257.
     (PTS 38253, No TPR, Severity 2)

     This defect is corrected in the source base, but is not part of the D10
     IPM20 release.

 29. Unshare of down filesystem hangs system shutdown.
     (PTS 38283, No TPR, Severity 2)

 30. EX NFS client: Node discovery of NFS mount with down NFS server can
     loop.
     (PTS 38359, No TPR, Severity 2)

 31. new_rem_swapfile() can deadlock with tnc_anon_resv_adjust() over
     registrar locks.
     (PTS 38390, No TPR, Severity 3)

     This can occur on the root node when it exhausts local swap and
     attempts to access swap on other nodes. Non-root nodes will not
     encounter this deadlock.

 32. EX NFS server: sharing of chard mount on non-lockd node will ASSERT on
     remote lockf.
     (PTS 38435, No TPR, Severity 2)

 33. EX NFS server: lockd can be hung on unavailable chard cluster mount.
     (PTS 38436, No TPR, Severity 3)

 34. Page table manipulation in kdb has bugs.
     (PTS 38523, No TPR, Severity 2)

 35. EX NFS client: Cluster must deal with size changes at NFS server
     correctly.
     (PTS 38530, No TPR, Severity 2)

 36. Nodedown needs to be run at higher priority.
     (PTS 38649, No TPR, Severity 2)

 37. Cnet Adapter Check causes the whole cluster to hang.
     (PTS 38666, No TPR, Severity 2)

 38. VXFS inode has a different generation number than CFS file handle.
     (PTS 38697, No TPR, Severity 2)

 39. wtmpx file has incomplete records after failover when
     tnc_rootopt=0x104000.
     (PTS 38748, No TPR, Severity 2)

 40. Get rid of tnc_rootopt in /stand/boot.
     (PTS 39134, No TPR, Severity 2)

     Currently, there is no way to specify mount options for the root
     filesystem, except through the tnc_rootopt bootstrap parameter which
     only allow the specification of the chard, charddup, and intr mount
     options. This means that there is no way to specify backup cache nodes
     for the root filesystem. As a workaround, the system will automatically
     use the secondary root node as the backup cache for the root
     filesystem. Additionally, if the secondary root node is not available,
     the system will automatically select another node in the cluster to
     provide the backup cache for the root filesystem. Please note that this
     auto-selection capability applies only to the root filesystem, i.e.
     only nodes specified via the bkup option to the mount command may
     become a backup cache for non-root filesystems.

     In the future, support will be added to use /etc/vfstab to determine
     the mount options for the root filesystem, e.g. to allow the explicit
     specification of its backup cache nodes.

 41. Spawndaemon does not validate data provided by daemon configuration
     files. If fields such as the name of the restart script are invalid,
     Keepalive would be unable to restart the daemon.
     (PTS 39574, No TPR, Severity 2)

 42. disksetup and diskadd man pages need changes for D10IPM20.
     (PTS 39829, No TPR, Severity 1)

     The disksetup and diskadd commands must be run on the node to which the
     disk is attached.

 43. pdiconfig man page needs changes for D10IPM20.
     (PTS 39830, No TPR, Severity 1)

     The pdiconfig command has a new option. The -T<node> flag can be
     specified with the -l option. This flag specifies the node about which
     to generate the configuration listing.

 44. diskformat fails with error: V_REMOUNT failed: device busy.
     (PTS 39831, No TPR, Severity 1)

     When diskformat is used on NonStop Clusters, an error is reported and
     the disk is not formatted. It is not necessary to run diskformat on
     Compaq Disks. If desired, you may run disksetup with the surface
     analysis option. However, this may take up to 10 hours.

 45. Hot add and hot remove of disks is not supported in NonStop Clusters.
     (PTS 39832, No TPR, Severity 1)

     NonStop Clusters does not support the Hot insertion or removal of disk
     devices feature of pdiadd. It is necessary to reboot the node for the
     new disks to be recognized. For RAID disks, the array must be
     configured offline using the Compaq Array Configuration Utility.
     pdi_hot.c is not clusterized

 46. pditimeout is not clusterized for NonStop Clusters.
     (PTS 39833, No TPR, Severity 1)

     The pditimeout command is not clusterized for NonStop Clusters. This
     command is used only for the root node and cannot be used for any
     dependent nodes. Compaq HBA do not support timeouts; this functionality
     is currently not applicable to Compaq disk subsystems.

 47. slow reboot/nodeup times when fully populated RAID on the node.
     (PTS 39932, No TPR, Severity 1)

     Slow nodeup occurs when nodeup processing begins before nodedown
     processing completes. If a node joins the cluster before nodedown
     processing is completed for that node, the node may take much longer to
     re-join the cluster.

     If you are experiencing this problem, the following actions may improve
     the time for a node to re-join.

     If the following appears in your /stand/<node>/boot files:

     AUTOBOOT=YES

     You may change this parameter in the /stand/<node>/boot file for each
     node to:

     AUTOBOOT=NO

     TIMEOUT=300

     The node will delay 300 seconds before it attempts to rejoin. This will
     insure that nodedown processing has completed before nodeup processing
     begins. You may change the "TIMEOUT" value to increase or decrease the
     autoboot delay to optimize the node join time for your cluster.

     If your cluster is booting very slowly, you may improve the boot time
     by booting the nodes 1 at a time.

                               End of Softdoc